## Slide 1: Fast, Unbiased Uncertainty Propagation with Multi-model Monte Carlo
Geoffrey Bomarito1, James Warner1, Samantha Nieomoeller1,2, Luke Morrill1, Patrick Leser1, William Leser1, Robert A. Williams1, Soumyo Dutta1
This material is a work of the U.S. Government and is not subject to copyright protection in the United States.
  NASA Langley Research Center, Hampton, VA
  University of California – Los Angeles, Los Angeles, CA

## Slide 2: Uncertainty Propagation
Initial Speed
Prob
Atm. Pressure
Prob
Prob
Wind direction
How does uncertainty in model inputs affect predictions of output?
Model
Inputs
Outputs
Probability
Input 1
Probability
Output 1
Probability
Landing Latitude
Model
Inputs
Outputs
Probability
Landing Longitude
Notes: So we set out to make it easy to compare methods and implement new ones, and ended up finding some improvements along the way

## Slide 3: Monte Carlo (MC) Simulation
Initial Speed
Prob
Atm. Pressure
Prob
Prob
Wind direction
Model
Inputs
Outputs
Initial Speed
Prob
Atm. Pressure
Prob
Prob
Wind direction
Probability
Landing Latitude
Probability
Landing Longitude
Let’s estimate expected value (i.e. expected landing location) using MC
1) Draw random inputs
3) Form estimator
Unbiased:
Model
2) Evaluate model
Solution Time:
HiFi model cost
Mean Squared Error = bias + variance

## Slide 4: Low-fidelity MC with Machine Learning (ML) Surrogates
How can we improve calculation time?
1) Draw random inputs
3) Form estimator
Unbiased:
Model
2) Evaluate model
Solution Time:
Model cost
ML Surrogate
Solution Time:
Surrogate cost << Model cost
Surrogate cost
Biased:
Mean Squared Error = bias + variance
bias irreducible error!

## Slide 5: Multi-model Monte Carlo
1) Draw random inputs
3) Form estimator
Model
2) Evaluate model
ML Surrogate
0
1
Constructed to be
Unbiased and Fast!
samples
samples

## Slide 6: Example: Multi-Level Monte Carlo MLMC
Main Idea: Use a surrogate and
correct with high-fidelity model
Solution Time:
Unbiased
Can Extend to More Models
Variance of difference of successive
models should be decreasing
[1]
[1] Giles, M B. Operations Research (2008)

## Slide 7: MLMC Results
Mean Squared Error
Accuracy in Expected Landing Location
More confidence with less time/resources

## Slide 8: MLMC Results
More confidence with less time/resources
Mean Squared Error
Accuracy in Expected Landing Location

## Slide 9: Approximate Control Variates (ACV)
1) Draw random inputs
3) Form estimator
Model
2) Evaluate model
Surrogate M
0
M
Surrogate 1
1
…
[2]
[2] Gorodetsky, A A., et al. Journal of Computational Physics (2020)
Unbiased
MSE = variance
  controlled by input subsets
Solution time
  controlled by input subsets
Goal: Sample allocation optimization
Find , , such that variance is minimal and cost is under budget

## Slide 10: Sample Allocation Optimization
adjusting size and overlap changes MSE and cost

## Slide 11: Sample Allocation Optimization
there are many configurations

## Slide 12: Sample Allocation Optimization
The domain of optimization is huge!
more complicated with more models

## Slide 13: Parametrically-defined ACV (PD-ACV)
Domain of all possible
ACV sample allocations
Other ACV allocations
MLMC allocations
Parametrically-defined allocations
global
optimum
[3]
[3] Bomarito, Geoffrey F., et al. arXiv preprint arXiv:2012.02750 (2020).
The best method is problem dependent,
but it’s better to search more area
PD-ACVs are generalized versions of existing methods that cover more allocations

## Slide 14: Random Model Scenarios
Choose number of models [2-6]
Sample random correlation matrix
Sample random variances
Sample random model costs (relative to hifi cost)
Perform allocation optimization for all algorithms (fixed cost budget)
~5 Million
PD-ACV
ACV
MLMC
Results Moving Forward: Multi-Model MC = PD-ACV

## Slide 15: Application
Program to Optimize Simulated Trajectories II (POST2) was used to model the flight trajectory
The accuracy of multi-model MC QoI estimates was quantified versus both high- and low-fidelity MC
Trajectory quantities of interest (QOIs) Considered
ADEPT SR-1 Test Flight Schematic [4]
[4] Dutta et al. AIAA Aviation 2019 Forum
Analysis of the Adaptable Deployable Entry & Placement Technology (ADEPT) Sounding Rocket 1 (SR-1) test flight
75 random input parameters; 15 QoIs

## Slide 16: Trajectory Simulation Models
Correlation of low-fidelity models with respect to the high-fidelity model
Model | Run Time (sec) | Speedup (X)
High Fidelity | 2.2 x 102 | 1.0 x 100
Reduced Physics | 4.7 x 101 | 4.6 x 100
Coarse Time Step | 2.8 x 100 | 7.8 x 101
Machine Learning | 7.0 x 10-4 | 3.1 x 105
Trajectory Simulation Model Run Times
High-fidelity model:
  POST2 with time step sec
Low-fidelity models:
  Reduced physics: POST2 with simplified atmosphere model
  Coarse time step: POST2 with sec
  Machine learning: Support vector machine (SVM) regression trained with input/output data from 250 POST2 simulations

## Slide 17: Estimator Variance Comparison
For a computational budget of 104 seconds, the sample allocation optimization was solved for two cases
  Vector Opt.: minimizes variance for all QoIs simultaneously
  Scalar Opt.: minimizes variance for each QoI individually
For a computational budget of 104 seconds,
Multi-Model MC Variance Reduction Vs. High-Fidelity MC

## Slide 18: Estimator Accuracy vs. Run Time
The MSE was calculated for high-, low-, and multi-model MC estimators versus a reference solution using high-fidelity MC with 100,000 samples
MSE versus Run Time for Several Trajectory QoIs
MSE
Run Time
Mean Squared Error (MSE) = bias + variance

## Slide 19: Estimator Accuracy vs. Run Time
The MSE was calculated for high-, low-, and multi-model MC estimators versus a reference solution using high-fidelity MC with 100,000 samples
MSE versus Run Time for Several Trajectory QoIs

## Slide 20: Estimator Accuracy vs. Run Time
The MSE was calculated for high-, low-, and multi-model MC estimators versus a reference solution using high-fidelity MC with 100,000 samples
MSE versus Run Time for Several Trajectory QoIs
Low-to-high fidelity model correlation
Higher correlations yield large accuracy improvement relative to high-fidelity MC
Lower correlations yield accuracy comparable to high-fidelity MC

## Slide 21: Conclusions & Future Work
Multi-model MC approach leverages speed of surrogate models combined with accuracy (unbiasedness) of high-fidelity models
Established the Multi-model MC approach to trajectory simulation as an alternative to standard MC that relies exclusively on a high- or low- fidelity model
Demonstrated the potential to deliver up to two orders of magnitude accuracy improvement
Future Work:
  Develop low-fidelity models that have higher correlation with respect to the high-fidelity model for dynamic trajectory QoIs
  Extend the multi-model MC approach to predict more advanced statistical quantities (probability distributions, rare event probabilities, landing ellipses, etc.)

## Slide 22: MXMCPy
The best method is problem dependent
github.com/nasa/MXMCPy
Simple interface to
  compare and use different algorithms
  implement new estimators

## Slide 23: Thank You
geoffrey.f.bomarito@nasa.gov
References:
[1] Giles, M. B., “Multilevel Monte Carlo path simulation,” Operations Research, Vol. 56, No. 3, 2008
[2] Gorodetsky, A., Geraci, G. , Eldred, M., and Jakeman, J. D., “A generalized approximate control variate framework for multifidelity uncertainty quantification,” Journal of Computational Physics, Vol. 408, 2020.
[3] Bomarito, G. F., Leser, P. E., Warner, J. E., and Leser, W. P., “On the optimization of approximate control variates with parametrically defined estimators,” arXiv preprint arXiv:2012.02750 (2020).
[4] Dutta, S., and Green, J. S., “Flight mechanics modeling and post-flight analysis of ADEPT SR-1,” AIAA Aviation 2019 Forum, AIAA, Dallas, TX, 2019.