## Slide 1: Estimating Pure-Error from Near Replicates in Design of Experiments
Caleb King
Research Statistician Developer
JMP Division, SAS Institute
Caleb.King@JMP.com
Thomas Bzik
Statistical Consultant
bziktj@verizon.net
DATAworks 2021, April 12-14, virtual
Peter Parker
National Aeronautics and Space Administration
Hampton, VA 23681
peter.a.parker@nasa.gov

## Slide 2: Pure-Error in Design of Experiments
Pure-error estimates are based on exact replicates - powerful and highly desirable in practice
  Serve as model-independent estimate of experimental variability
  A key component in Lack-of-Fit testing
  Very easy to explain and approachable to non-statisticians
In practice, precise genuine replicates are often not achievable
  We often lack control precision/efficiency to set the factor levels (independent variable)
It is often much easier to measure the actual factor levels of intended replicates, resulting in “near replicates”

## Slide 3: Relevant in Characterization Experiments
High-precision measurement systems with accurate set-point measurements (feedback/monitor), but not controlled
Lack of fit is important to isolate in the total uncertainty (residual)
Guides strategic investment in improving calibration models
  Invest in the apparatus
  Explore high-order designs/models

## Slide 4: Some Approaches in the Literature
Montgomery, Martin, and Peck (1980), "Interior Analysis of the Observations in Multiple Linear Regression," Journal of Quality Technology, 12(3), pg. 165-173.
Joglekar, Schuenemeyer, and LaRiccia (1989), “Lack-of-Fit Testing When Replicates are not Available,” The American Statistician, 43(3), pg. 135-143.
Su and Yang (2006), “A Note on Lack-of-Fit Tests for Linear Models Without Replication,” Journal of the American Statistical Association, 101, pg. 205-210
Christensen (1989) “Lack-of-Fit Test Based on Near or Exact Replicates,” The Annals of Statistics, 17, pg. 673-683.
Christensen and Sun (2010) “Alternative Goodness-of-Fit Tests for Linear Models,” Journal of the American Statistical Association, 105, pg. 291-301.
In practice, none have been satisfactory solutions, nor are they widely used

## Slide 5
WHAT CAN BE DONE WITH NEAR REPLICATES?
Naïve Approach
Just pretend they are true replicates
  Could lead to overestimation of PE depending on the transfer function from x to y.
Residual Adjusted Approach
Adjust the near replicates to be estimated pure replicates.
  This is the methodology we propose.

## Slide 6: Presentation Outline
Introduce our methodology to convert Near replicates to Estimated replicates
Present a Theoretical Justification for our methodology
Conduct a Simulation Study to test methodology performance and robustness
Summary and Practitioner Guidance

## Slide 7
RESIDUAL ADJUSTED APPROACH: DESCRIPTION
Fit the assumed regression model
Identify the set(s) of near replicates (typically the intended replicates)
For each set of near replicates:
  Calculate the average of the near replicates ()
  Use the regression model to correct each point’s observed response to the estimated response at the average ()
  Use these corrected values to estimate PE for each set
  Pool PE estimates if there are multiple sets of near replicates
Corrected values are only used for PE estimation, nothing else

## Slide 8
RESIDUAL ADJUSTED APPROACH : BASIC VISUALIZATION
Regression Model to be Tested for LOF
Intended Replicates
X
Y
Average
The point on the right will be adjusted downward by the impact of slope difference from the local average.
The point on the left will be adjusted upward by the impact of slope difference from the local average.
The middle point will be barely adjusted upward.
Notes: After the adjustment, the local Y variation from the estimated model is removed.
(is this phrase still needed?)

## Slide 9
RESIDUAL ADJUSTED APPROACH : BASIC VISUALIZATION
Typically Less Variation in This View
Naive Approach View
Pretend All at the Same X
Residual Adjusted View
Corrected by Model to Same X
Near Replicate View
Typically Excessive Variation in This View

## Slide 10
RESIDUAL ADJUSTED APPROACH : SIMPLE EXAMPLE
True Model: Y = 10 + 5X (without any simulated error)
Fitted Model: Y = 10 + 5X
The near replicates were three attempts to get X=2
Naïve estimate of PE variance = Variance (19, 20, 21) = 1
Average of Near Replicates = Mean(1.8, 2.0, 2.2) = 2.0
(In practice, the center of mass will rarely be equal to the target)
X Offset = Average - X
Adjust Amount = X offset * est. slope = X offset * 5
Adjusted Y = Y + Adjust Amount
Corrected PE variance = Variance (20, 20, 20) = 0
Correction for more complex models uses all slope estimates involving X in the model
X | Y
1.0 | 15.0
1.8 | 19.0
2.0 | 20.0
2.2 | 21.0
3.0 | 25.0
X | Y | X Offset | Adjust Amount | Adjusted Y
1.8 | 19.0 | 0.2 | 1 | 20.0
2.0 | 20.0 | 0.0 | 0 | 20.0
2.2 | 21.0 | -0.2 | -1 | 20.0

## Slide 11: Theoretical justification: Notation
Let’s assume a quadratic model:
Consider a near replicate point
  represents the known deviation from the intended level
We can represent a vector of near replicate points as
  is the vector of intended replicate design points
  is the “design matrix” of residuals from the intended levels
  is an “adjustment matrix” to allow for addition of to (essentially a Jacobian matrix)
The theory will hold for any higher polynomial model as well.

## Slide 12: Theoretical justification: Pure-error estimate
The general pure-error estimate is represented as
  is the R-dimensional identity matrix
  is an R x R matrix of 1’s
If , then this will give the naïve estimate.
If , then this will give the residual adjusted estimate.

## Slide 13: Theoretical justification: Comparison
Naïve Method
Expectation of Pure-Error Estimate
Bias-Correction
  Let represent the additive bias.
Residual Adjusted Method
Expectation of Pure-Error Estimate
The Residual Adjusted Method is a natural correction to the naïve method.

## Slide 14: Theoretical justification: additional notes
Since the multiplicative bias is less than or equal to 1, it indicates that the residual adjusted estimator tends to underestimate the true pure-error.
The standard residual adjusted method can also be bias-corrected, by simply dividing by the multiplicative bias.
The distribution of the residual adjusted bias-corrected pure-error estimator, while not known to closed form, can be approximated with a chi-squared distribution with degrees of freedom equal to the trace of the multiplicative bias.

## Slide 15: Simulation study: outline of study
We conducted a simulation study to explore further the behavior of the residual adjusted method in comparison with the naïve method.
Scenario 1: Simple Linear Model (for baseline illustration)
  Two 6-run designs; one with 3 replicate centerpoints, one with 3 replicate “edgepoints” (X=1)
  Assess pure-error estimate
Scenario 2: Three-Factor Multivariate Model with Interaction
  Three 15-run Central Composite Designs; two with replicate centerpoints (3 and 5 times), one with 3 replicate edgepoints (X1=1,X2=1,X3=1)
  Assess pure-error estimate and Type I error for LOF testing (target is 5%)
Scenario 3: Three-Factor Multivariate Model with Interaction and Quadratic
  Same designs as Model 2
  Quadratic term is not fit, resulting in true LOF
  Assess pure-error estimate and power for detecting LOF
Scenario 4: More Extreme LOF
  Same designs
  Additional interaction and quadratic terms not fit; increase error variance
  Assess pure-error estimate and power for detecting LOF
For each model, we will assess sensitivity of the pure-error estimates to range deviation, the standard deviation around the target value.

## Slide 16
In the simulations, we will only consider range deviations within its realm of likely application.
Higher dimensional models will only be examined in a more rational range
Simulation study: outline of study
Range Deviation | Rational?
0 | NA
0.01 | Yes
0.05 | Yes
0.1 | Maybe
0.2 | Stretch
0.5 | No
1 | No

## Slide 17: Simulation study: scenario 1 pure-error estimates
3 Replicate Centerpoints
Range Deviation | Naïve Method | Residual Adjusted Method | Bias-Corrected Residual Adjusted Method
0 | 0.9996 | 0.9996 | 0.9996
0.01 | 1.0342 | 1.0008 | 1.0009
0.05 | 1.7302 | 0.9986 | 0.9996
0.1 | 4.7033 | 0.9954 | 1.0001
0.2 | 10.9948 | 0.9856 | 0.9993
3 Replicate Edgepoints
Range Deviation | Naïve Method | Residual Adjusted Method | Bias-Corrected Residual Adjusted Method
0 | 1.0003 | 1.0003 | 1.0003
0.01 | 1.0385 | 1.0002 | 1.0002
0.05 | 1.8178 | 0.9988 | 0.9994
0.1 | 5.5359 | 0.9953 | 0.9984
0.2 | 13.6601 | 0.9856 | 1.0004
True Model:

## Slide 18: Simulation study: scenario 2 pure-error estimates
3 Replicate Centerpoints
Range Deviation | Naïve Method | Residual Adjusted Method | Bias-Corrected Residual Adjusted Method
0 | 1.0007 | 1.0007 | 1.0007
0.01 | 1.0490 | 1.0008 | 1.0008
0.05 | 1.4317 | 0.9985 | 0.9993
0.1 | 7.0097 | 0.9939 | 0.9971
0.2 | 14.1136 | 0.9869 | 1.0004
3 Replicate Edgepoints
Range Deviation | Naïve Method | Residual Adjusted Method | Bias-Corrected Residual Adjusted Method
0 | 1.0010 | 1.0010 | 1.0010
0.01 | 1.0928 | 1.0002 | 1.0004
0.05 | 2.4154 | 0.9953 | 0.9991
0.1 | 5.8832 | 0.9912 | 1.0006
0.2 | 34.2235 | 0.9489 | 1.0012
True Model:

## Slide 19: Simulation study: scenario 2 Type I Error Rates
3 Replicate Centerpoints
Range Deviation | Naïve Method | Bias-Corrected Residual Adjusted Method
0 | 0.0498 | 0.0498
0.01 | 0.0483 | 0.0498
0.05 | 0.0365 | 0.0497
0.1 | 0.0069 | 0.0497
0.2 | 0.0056 | 0.0483
3 Replicate Edgepoints
Range Deviation | Naïve Method | Bias-Corrected Residual Adjusted Method
0 | 0.0499 | 0.0499
0.01 | 0.0469 | 0.0502
0.05 | 0.0224 | 0.0495
0.1 | 0.0136 | 0.0489
0.2 | 0.000029 | 0.0436
True Model:

## Slide 20: Simulation study: scenario 2 pure-error estimates and Type I Error Rates
5 Replicate Centerpoints
Range Deviation | Naïve Method | Residual Adjusted Method | Bias-Corrected Residual Adjusted Method
0 | 0.9993 | 0.9993 | 0.9993
0.01 | 1.0421 | 1.0006 | 1.0006
0.05 | 1.7824 | 0.9989 | 0.9996
0.1 | 6.5091 | 0.9984 | 1.0015
0.2 | 20.8881 | 0.9892 | 1.0014
Range Deviation | Naïve Method | Bias-Corrected Residual Adjusted Method
0 | 0.0502 | 0.0502
0.01 | 0.0473 | 0.0497
0.05 | 0.0216 | 0.0498
0.1 | 0.0021 | 0.0499
0.2 | < | 0.0483
Range Deviation | Naïve Method | Bias-Corrected Residual Adjusted Method
0 | 0.0502 | 0.0502
0.01 | 0.0473 | 0.0497
0.05 | 0.0216 | 0.0498
0.1 | 0.0021 | 0.0499
0.2 |  | 0.0483
True Model:

## Slide 21: Simulation study: scenario 3 pure-error estimates
3 Replicate Centerpoints
Range Deviation | Naïve Method | Residual Adjusted Method | Bias-Corrected Residual Adjusted Method
0 | 0.9983 | 0.9983 | 0.9983
0.01 | 1.0316 | 1.0012 | 1.0012
0.05 | 1.5899 | 1.0009 | 1.0016
0.1 | 3.6500 | 1.0107 | 1.0134
0.2 | 12.2593 | 1.4461 | 1.4703
3 Replicate Edgepoints
Range Deviation | Naïve Method | Residual Adjusted Method | Bias-Corrected Residual Adjusted Method
0 | 1.0008 | 1.0008 | 1.0008
0.01 | 1.0544 | 1.0064 | 1.0065
0.05 | 2.7183 | 1.1770 | 1.1816
0.1 | 3.8995 | 1.5651 | 1.5773
0.2 | 29.6467 | 2.3621 | 2.4873
True Model:

## Slide 22: Simulation study: scenario 3 power to detect lack-of-fit
3 Replicate Centerpoints
Range Deviation | Naïve Method | Bias-Corrected Residual Adjusted Method
0 | 0.8011 | 0.8011
0.01 | 0.7878 | 0.7977
0.05 | 0.6386 | 0.7955
0.1 | 0.3281 | 0.7721
0.2 | 0.1132 | 0.6732
3 Replicate Edgepoints
Range Deviation | Naïve Method | Bias-Corrected Residual Adjusted Method
0 | 0.8113 | 0.8113
0.01 | 0.7964 | 0.8114
0.05 | 0.4025 | 0.7391
0.1 | 0.3328 | 0.6224
0.2 | 0.0426 | 0.4026
True Model:

## Slide 23: Simulation study: scenario 3 pure-error estimates and power
5 Replicate Centerpoints
Range Deviation | Naïve Method | Residual Adjusted Method | Bias-Corrected Residual Adjusted Method
0 | 0.9994 | 0.9994 | 0.9994
0.01 | 1.0542 | 1.0001 | 1.0002
0.05 | 2.6239 | 1.0003 | 1.0012
0.1 | 5.7257 | 1.0025 | 1.0053
0.2 | 16.8530 | 1.1639 | 1.1796
Range Deviation | Naïve Method | Bias-Corrected Residual Adjusted Method
0 | 0.9996 | 0.9996
0.01 | 0.9992 | 0.9995
0.05 | 0.8956 | 0.9994
0.1 | 0.5504 | 0.9989
0.2 | 0.0131 | 0.9907
True Model:

## Slide 24: Simulation study: scenario 4 pure-error estimates
3 Replicate Centerpoints
Range Deviation | Naïve Method | Residual Adjusted Method | Bias-Corrected Residual Adjusted Method
0 | 3.9993 | 3.9993 | 3.9993
0.01 | 4.0255 | 3.9939 | 3.9939
0.05 | 5.5235 | 3.9994 | 4.0020
0.1 | 6.4455 | 4.0071 | 4.0172
0.2 | 28.1179 | 4.1196 | 4.1898
3 Replicate Edgepoints
Range Deviation | Naïve Method | Residual Adjusted Method | Bias-Corrected Residual Adjusted Method
0 | 4.0009 | 4.0009 | 4.0009
0.01 | 4.1046 | 4.0079 | 4.0088
0.05 | 5.0234 | 4.2254 | 4.2354
0.1 | 7.8110 | 5.4974 | 5.5712
0.2 | 43.5795 | 9.7558 | 10.5807
True Model:

## Slide 25: Simulation study: scenario 4 power to detect lack-of-fit
3 Replicate Centerpoints
Range Deviation | Naïve Method | Bias-Corrected Residual Adjusted Method
0 | 0.3200 | 0.3200
0.01 | 0.3186 | 0.3208
0.05 | 0.2408 | 0.3164
0.1 | 0.2069 | 0.3153
0.2 | 0.0544 | 0.3369
3 Replicate Edgepoints
Range Deviation | Naïve Method | Bias-Corrected Residual Adjusted Method
0 | 0.3429 | 0.3429
0.01 | 0.3355 | 0.3417
0.05 | 0.2919 | 0.3304
0.1 | 0.1955 | 0.2652
0.2 | 0.0376 | 0.1104
True Model:

## Slide 26: Simulation study: scenario 4 pure-error estimates and power
5 Replicate Centerpoints
Range Deviation | Naïve Method | Residual Adjusted Method | Bias-Corrected Residual Adjusted Method
0 | 4.0043 | 4.0043 | 4.0043
0.01 | 4.0523 | 3.9999 | 4.0001
0.05 | 5.3547 | 3.9978 | 4.0009
0.1 | 8.1995 | 3.9994 | 4.0114
0.2 | 28.0967 | 4.0609 | 4.1154
Range Deviation | Naïve Method | Bias-Corrected Residual Adjusted Method
0 | 0.6956 | 0.6956
0.01 | 0.6911 | 0.6980
0.05 | 0.5596 | 0.7096
0.1 | 0.3220 | 0.6650
0.2 | 0.0581 | 0.6216
True Model:

## Slide 27
SUMMARY
In practice, it is more common to record near replicate levels than enforce exact replicates.
The residual adjusted approach is a simple, natural correction adjustment of the naïve approach in estimating pure-error from near replicates.
In the absence of LOF, the bias-corrected residual adjusted method will generate a consistent, unbiased estimate of pure-error. It also maintains a stable Type I error compared to the naïve method.
In the presence of LOF, the bias-corrected residual adjusted method is less sensitive to range deviation than the naïve method. It also tends to have significantly more power in detecting LOF.