## Slide 1: MITIGATING PILOT DISORIENTATION WITH SYNTHETIC VISION DISPLAYS
Kathryn Ballard
Trey Arthur
Kyle Ellis
Renee Lake
Stephanie Nicholas
Lance Prinzel

## Slide 2: What is the problem? Why NASA? What are synthetic vision displays? How were they tested? How did pilot subjects affect testing and analysis?

## Slide 3
Boeing Statistical Summary of Commercial Jet Airplane Accidents Worldwide Operations, 2016
Chart: Number of Fatal Accidents
| Fire/Smoke (Non-Impact) | Runway Excursion (Takeoff) | Ground Handling | Unknown | Wind Shear or Thunderstorm | System/Component Failure or Malfunction (Powerplant) | Midair/Near Midair Collision | Runway Excursion (Landing) + Abnormal Runway Contact + Undershoot/Overshoot | Controlled Flight into or Toward Terrain | Loss of Control - In Flight
Series 1 | 2 | 3 | 7 | 2 | 1 | 2 | 3 | 14 | 14 | 15
Chart: Number of Onboard Fatalities
| Fire/Smoke (Non-Impact) | Runway Excursion (Takeoff) | Ground Handling | Unknown | Wind Shear or Thunderstorm | System/Component Failure or Malfunction (Powerplant) | Midair/Near Midair Collision | Runway Excursion (Landing) + Abnormal Runway Contact + Undershoot/Overshoot | Controlled Flight into or Toward Terrain | Loss of Control - In Flight
Series 1 | 4 | 6 | 7 | 85 | 96 | 153 | 154 | 632 | 658 | 1396
Fatal Accidents | Worldwide Commercial Jet Fleet | 2006 to 2015

## Slide 4
Boeing Statistical Summary of Commercial Jet Airplane Accidents Worldwide Operations, 2006
Chart: Number of Onboard Fatalities
| Aerodrome | Wind Shear or Thunderstorm | Runway Incursion | Midair Collision | Icing | Unknown or Undetermined | Fuel Related | Other | System/Component Failure or Malfunction (Powerplant) | Runway Excursion + Undershoot/Overshoot + Abnormal Runway Contact | Fire/Smoke (Non-Impact) | System/Component Failure or Malfunction (Non-Powerplant) | Loss of Control - In Flight | Controlled Flight Into or Toward Terrain
Series 1 | 1 | 48 | 110 | 144 | 159 | 165 | 245 | 298 | 489 | 563 | 618 | 862 | 2830 | 3735
Fatal Accidents | Worldwide Commercial Jet Fleet | 1987 to 2005
Chart: Number of Fatal Accidents
| ADRM | Wind Shear or Thunderstorm | Runway Incursion | Midair Collision | ICE | Unknown or Undetermined | FUEL | Other | System/Component Failure or Malfunction (Powerplant) | runway +USOS+ARC | Fire/Smoke (Non-Impact) | System/Component Failure or Malfunction (Not Powerplant) | Loss of Control - In Flight | Controlled Flight Into or Toward Terrain
Series 1 | 1 | 3 | 3 | 2 | 6 | 3 | 9 | 4 | 15 | 70 | 10 | 12 | 39 | 57

## Slide 6
Airplane State Awareness (ASA)
Joint Safety Analysis Team (JSAT)
Majority of these accidents involved loss of attitude (spatial disorientation) and/or loss-of-energy state awareness
STUDIED 18 LOSS OF CONTROL – IN FLIGHT ACCIDENTS AND INCIDENTS (2001-2010)
Design and research “Virtual Day-VMC” or “Synthetic Vision” display technologies

## Slide 7
upload.wikimedia.org/wikipedia/commons/4/44/Boeing_787-8_N787BA_cockpit.jpg
Traditional Blue-Over-Brown vs Synthetic Vision Display

## Slide 8: Synthetic Vision Displays

## Slide 9: AFDC Research Questions
Do synthetic vision displays improve spatial awareness during unusual attitudes?
www.linkaviation.com/images/410_unusual_attitude.jpg

## Slide 10: AFDC Research Questions
Do synthetic vision displays improve spatial awareness during unusual attitudes?
How should synthetic vision displays be presented?
Can synthetic vision displays provide enough visual dominance to overcome physical illusions?

## Slide 11
2018
2015
2017
2016
Attitude Recognition
MARCH
JULY
Design of Virtual Day-VMC Displays
MAY
Attitude Awareness – UARs and SPOT Scenarios
Energy and Attitude State – Extreme Upsets and Recovery
JANUARY
APRIL/MAY
Low-Hour and International Pilots UARs and LOFT Scenarios
APRIL
Display Transition During Recovery
Head-Up and Head-Worn Display Simulator and Flight Test
AUGUST

## Slide 12: NASA Langley Experiment Keep or remove synthetic vision during unusual attitude recovery
Experiment Design
Balancing act between:
  Facility schedule
  Available pilots
Tested 12 pilots, around 1.5 hours each
  Able to complete a repetition of the run matrix

## Slide 13: NASA Langley Experiment Keep or remove synthetic vision during unusual attitude recovery
Keep synthetic vision during unusual attitudes | 
Pull synthetic vision during unusual attitudes | 
Baseline | 
Each pilot flew 4 unusual attitude recoveries at different orientations at each of three display configurations, then repeated everything

## Slide 14: Analysis Methods
A variety of mixed models were used to test the hypothesis of the form:
Model:
Linear mixed model | Continuous normal variables | Max roll, max pitch, max alpha, delta altitude, delta speed
Generalized linear mixed model with a log link | Time to event variables | Time to first pitch input, time to first roll input, Time to first correct roll
Generalized linear mixed model, Poisson family | Discrete count variable | Number of roll reversals
Cumulative link mixed model | Ordered discrete variable | Total UAR score
α = 0.05/12 = 0.004

## Slide 15: Boeing Facility Experiment Synthetic Vision vs Blue-over-Brown with International Pilots
Experiment Design
Balancing act between:
  Boeing facility schedule
    Nearly all time slots were midnight – 4am
  Researcher staffing
  International pilots
    There was a pilot strike before testing was supposed to start
Worked with 12 crews, two hours each
  Limited the number of unusual attitude recoveries (no repetition – less power)

## Slide 16: Boeing Facility Experiment Synthetic Vision vs Blue-over-Brown with International Pilots
Synthetic Vision | 
Baseline | 
Each crew flew 4 unusual attitude recoveries at different orientations at two display configurations

## Slide 17: Analysis Methods
Two mixed models will be used to test the hypothesis of the form:
Model:
Linear mixed model | Continuous normal variables | Max roll, max pitch, max alpha, delta altitude, delta speed
Generalized linear mixed model with a log link | Time to event variables | Time to first pitch input, time to first roll input, Time to first correct roll
Generalized linear mixed model, Poisson family | Discrete count variable | Number of roll reversals
Cumulative link mixed model | Ordered discrete variable | Total UAR score
Subjective questionnaire data may give more insights.

## Slide 18: DRD Facility Experiment Synthetic Vision with Background Attitude Indicator vs Blue-over-Brown
Experiment Design
Balancing act between:
  DRD Facility
  Pilot availability
  Pilot fortitude
    Subjected to vestibular illusions and up to 3g’s of force during each unusual attitude recovery
We plan to recruit 24 pilots who will spend around six hours at the facility
Disorientation
Research Device

## Slide 19: DRD Facility Experiment Synthetic Vision with Background Attitude Indicator vs Blue-over-Brown
Daily Experiment Schedule
Pilot 1 completes unusual attitude recoveries
Pilot 2 joins Pilot 1 for a Special Purpose Orientation Training run
Pilot 1 completes illusion runs
Pilot 2 completes unusual attitude recoveries
Pilot 2 completes illusion runs

## Slide 20: DRD Facility Experiment Synthetic Vision with Background Attitude Indicator vs Blue-over-Brown
Synthetic vision | 
Background attitude indicator | 
Baseline | 
Each pilot will fly 4 unusual attitude recoveries at different orientations at each of three display configurations, then repeat everything.

## Slide 21: Analysis Methods
Mixed models will be used to test the hypothesis of the form:
Model:
Linear mixed model | Continuous normal variables | Max roll, max pitch, max alpha, delta altitude, delta speed
Generalized linear mixed model with a log link | Time to event variables | Time to first pitch input, time to first roll input, Time to first correct roll
Generalized linear mixed model, Poisson family | Discrete count variable | Number of roll reversals
Cumulative link mixed model | Ordered discrete variable | Total UAR score

## Slide 22: AFDC Experiment Series Summary
Data collection and analysis still ongoing
Very positive feedback from pilots
Test Planning
  Consider facility and pilot constraints
Analysis
  Each pilot has a unique recovery style so a mixed effects model is appropriate
  With pilot as a random effect, each pilot’s performance is compared to themselves

## Slide 23: Questions?
Disorientation Research Device video – “Kraken”
Wright-Patterson Air Force base in Dayton, OH

## Slide 24: Back up slides

## Slide 25: Langley Experiment Results
The initial orientation of the aircraft was a bigger factor than display type in some metrics of interest
  Max roll
  Max pitch
  Delta altitude
Initial roll degree

## Slide 26: Langley Experiment Results
Most incorrect roll inputs happened in nose up scenarios
Not enough data to compare displays

## Slide 27
Boeing Experiment: Pilot Workload by Orientation