## Slide 1: JEDIS JMP Experimental Design Iterative Solver
JMP Experimental Design Iterative Solver

## Slide 2: What is JEDIS?
JEDIS is a JMP Add-In for automating
Design of Experiments (DOE) power calculations

## Slide 3: JEDIS simplifies answering questions like the following:
Typical Researchers
How many runs does my DOE need for 90% power across my factor-space?

## Slide 4: Traditional DOE methods require iterative estimation to size a design for a specific power
Repeat until design provides desired power
Define factors
and levels
Estimate design size required*
Determine if power is sufficient
  * For factorial designs: the number of design replications
  For optimal designs: the number of individual samples

## Slide 5: JEDIS iterates through designs for you
Define factors and levels
Define input ranges
Run JEDIS
Select design
  Inputs Ranges:
  Number of replicates/runs
  Signal-to-Noise Ratio
  Alpha (1-Confidence)

## Slide 6: Consider this motivational problem:
How many shots must the archer take to show, with confidence, his ability to hit the target’s center under varying conditions?

## Slide 7: The first step for all DOEs is defining factors and levels
Range
Angle
Miss distance
Response | Factors | Levels
Miss distance from center | Range from target | 10 m
 |  | 30 m
 |  | 50 m
 | Angle of shot | 15°
 |  | 30°
 |  | 45°
 |  | 60°

## Slide 8: Lets walk through JEDIS for this example archery DOE
Step 1
Open JEDIS and choose “Make Full Factorial Design”
Step 2
Construct DOE by adding factors and levels as normal in JMP
Step 3
Specify ranges for parameters and then let JEDIS run

## Slide 9: Video demo of JEDIS for archery DOE, in real time

## Slide 10: Recall our original motivation for JEDIS:
Typical Researchers
How many runs does my DOE need for 90% power across my factor-space?

## Slide 11: For this example, 90% power across all factors is possible at 80% confidence with 132 shots for a SNR of 1
90% power
80% conf.
1 SNR
132 shots

## Slide 12: Lets explore the default JEDIS plot and some other plotting options available to you in JMP

## Slide 13: JEDIS (Light) also works for pre-made designs
Perhaps you read a design in a test-planning document and you’d like to explore it over a range of SNR and Alpha

## Slide 14: JEDIS Light follows the same general procedure as JEDIS

## Slide 15: Wrap up: JEDIS is an easy to use tool for DOE automation
 Fully GUI based
 Enables exploration of design replicates, SNR, and alpha
 Allows DOE construction on-the-fly or loading from script
 Handles full factorial, D/I/α-optimal, and disallowed combinations
 Writes results in easy to use format (Tidy data)
 Automatically generates interactive data visualizations

## Slide 16: Step-by-step instructions and detailed documentation accessible from JEDIS main menu
10
9
8
7
6
5
4
3
2

## Slide 17
Questions?

## Slide 18
Remaining slides are back up.
JEDIS how-to and extra notes.

## Slide 19
How to use JEDIS

## Slide 20: Step 1: Select JEDIS from JMP Add-Ins menu*
Step 2: Choose type of DOE to run, or load a design script
*See final slide for JEDIS installation instructions

## Slide 21: Step 3: Follow normal JMP procedures to set up DOE
Factors
Levels
Model Terms
Disallowed combinations
Clicking ‘Make Design’ will run the JMP design builder, not JEDIS. Click ‘Run JEDIS’ instead.

## Slide 22: Step 4: Specify parameters for power calculations

## Slide 23: Step 5: After running, view and save results

## Slide 24: Step 6: Now you have your data – explore as you please!
Data saved in Tidy format
One variable per column & One observation per row

## Slide 25
How to use JEDIS Light

## Slide 26: Step 1: Open your design table in JMP

## Slide 27: Step 2: Run JEDIS Light from JMP Add-Ins menu
Step 3: Verify table formatting & specify parameters

## Slide 28: Step 4: Specify the model, add interactions if desired

## Slide 29: Step 5: View and save results, just like in JEDIS

## Slide 30
Extra Notes and Tips

## Slide 31: JEDIS add-in menu advanced options
From the JEDIS Advanced Options menu
you can replot any saved JEDIS data
and modify any default JEDIS parameters

## Slide 32: JEDIS parameter advanced options
Change Anticipated Coefficients
Allows you to select the alternative hypotheses with which JEDIS will test your DOE
Set Random Seed
Allows you to specify the random seed used for design generation
Adjust Custom Design Search Time
Allows you to specify how long JMP will search for an optimal solution to a design
Notes: Much more detail in documentation
Change Anticipated Coefficients
JMP’s default approach is a straightforward means to generating an alternative hypothesis of a specified effect size, but can result in an optimistic estimate of the power to distinguish between a factor's levels.
The Most Conservative Power (MCP) alternative hypothesis is the hypothesis that results in the least power for a specified effect size. While an exact MCP exists for a given design, its computation is not implemented in JMP, so JEDIS approximates it.

## Slide 33: How to save a DOE script in JMP in three clicks
1.
2.
3.

## Slide 34: Notes about saving scripts
Saving must be done before pressing the “Run JEDIS” button!
Saving a script is a JMP feature available in ANY window.
Saving scripts is not specific to JEDIS, but right now it is the only way to save a DOE for later use.

## Slide 35: How to change JMP’s custom design optimality criterion
1.
2.
3.
JEDIS uses JMP’s recommended optimality criterion by default, but you can select the type you want when you construct your DOE.

## Slide 36: How to install the JEDIS JMP Add-In
Method 1: Install from the Add-In file (works if your computer recognizes .jmpaddin files)
Double click the Add-In
Click “Install” when prompted
Method 2: Open the Add-In from JMP
Select File –> Open from JMP
Open the Add-In file
Click “Install” when prompted
(see method 1)