## Slide 1: Estimating the time of sudden shift in the location or scale of ergodic-stationary processes in SPM applications
Presented by: Zhi Wang
Co-Author: Marcus Perry
Defense and Aerospace Test and Analysis Workshop
April 26-28, 2022

## Slide 2
Introduction and Motivation
Modern industrial process Requirements: Advances in data acquisition and storage technology have permitted data to be sampled at a high rate, often inducing autocorrelation into the observed data sequences. In addition, today’s processes rarely follow the Normal distribution, making the use of traditional estimators that has unrealistic assumptions questionable
Limitations of the change point estimation strategies in the literature: The lack of a suitable change point estimation method in the case of autocorrelation is an important gap in the statistical process control (SPC) literature. For example, the popular maximum likelihood change point estimator for the time of step change in the mean of a normal process developed by Pignatiello and Samuel fails to consider the autocorrelation; Although Perry and Pignatiello extended this estimator to consider covariance-stationary autocorrelated process, it is still restricted by the normality assumption. As a result, today’s process stimulate the need for distribution-free strategies that consider autocorrelation
Focus: Estimating the time of step change in the location and/or scale of ergodic-stationary sequences following a genuine signal from a SPC chart. In which, a sequence is ergodic-stationary if depends on and as . Obtaining an accurate and reliable estimate of the process change point would permit a simplified search for and identification of the special cause in post control-chart signal diagnostic
Defense and Aerospace Test and Analysis Workshop
Zhi Wang
April 27, 2022
2/10
Introduction and Motivation

## Slide 3
A distribution-free joint monitoring scheme for location and scale using individual observations:
Define a median clipped binary sequence and an interquartile clipped binary sequence of the continuous data sequence is generated for each , where and . We then model the joint mass function for the clipped binary sequences using the Bahadur approximation proposed by Bahadur (1961). As a result, we proposed a CUSUM strategy for monitoring the mean of ergodic-stationary binary sequences. Our CUSUM charting statistic was derived from the sequential probability ratio test (SPRT) for testing the simple hypotheses versus , where
For and , the charting statistics:
Defense and Aerospace Test and Analysis Workshop
Zhi Wang
April 27, 2022
3/10
Introduction and Motivation
is the observed value of the binary sequence at time
first- order dependence structure
second-order dependence structures:
’s denoting the autocorrelation coefficients and
Next, we consider estimating the time of sudden shift in the mean μ of an ergodic-stationary binary sequence following a genuine signal from this CUSUM control chart

## Slide 4
Methodology
Consider the binary sequence where for . Denote an unknown change point such that for and for , where Assume the in-control mean is known and the shifted mean is unknown. Given an observed following a control chart signal, the objective is to estimate the unknown change point
Built-in change point estimator of the CUSUM control chart suggested by Page: The CUSUM change point estimate is given by the most recent time index yielding a cumulative sum of zero, that is
Maximum likelihood estimator (MLE) for the process change point: Using the MLE in place of the built-in CUSUM change point estimator allows the user to construct an approximate confidence set on the unknown change point , which is more useful than point estimates in practice as they provide additional information about the variability in the point estimate
Defense and Aerospace Test and Analysis Workshop
Zhi Wang
April 27, 2022
4/10
Methodology
Example: Single realization of a CUSUM sequence with the alarm threshold set to h=4. Control chart signaled at sample 114. The built-in CUSUM change point estimator yields = 98, which is the most recent time index yielding a cumulative sum of zero

## Slide 5
Let and :
First-order dependence: the log-likelihood function can be written explicitly as
where and . Since is unknown, it must be estimated from the data. However, unless , there is no closed-form solution for . Fortunately, given today’s computing capability, we can apply widely accessible optimization routines to numerically solve for at each . Denote the MLE of at any given by Then replacing with in above log-likelihood function and evaluating over all possible change points leads to the MLE for . That is,
One can easily extend the MLE for t to consider a higher-order dependence. We consider only the first-order dependence case in our following study, although higher-order dependence cases could be applied similarly
Defense and Aerospace Test and Analysis Workshop
Zhi Wang
April 27, 2022
5/10
Methodology

## Slide 6
Performance and Recommendation
Use Monte Carlo simulation to compare relative performances between the CUSUM, proposed and Perry and Pignatiello change point estimators for location (scale) shifts and following a genuine signal from the median-clipped (IQR-clipped) CUSUM chart of Perry and Wang. Specifically, We considered the CUSUM control chart to monitor the clipped sequence and designed the CUSUM chart for a 50% increase in the mean, i.e., μ0 = 0.5 and * = 0.75
We consider the continuous AR(1) model in our simulation, i.e., , where , and generate the median- and IQR-clipped sequences from this process. To assess the robustness of any given method across different white noise error distribution, we consider generating in the AR(1) model from the Pearson family of distribution
Defense and Aerospace Test and Analysis Workshop
Zhi Wang
April 27, 2022
6/10
Performance and Recommendation
Simulate a continuous in-control AR(1)
Length: M
Parameter:
error term: Pearson distribution with zero mean, unit variance and skewness parameter
In-control level parameter
Kurtosis of Pearson error distribution = , when , we have the standard normal distribution
Median-clipped sequences
IQR-clipped sequences
Estimate correlation parameters in Bahadur model
Autoregressive parameter and level parameter for the Perry and Pignatiello estimator
Estimate quartiles
MLE
In-control process
Monitoring began…
Change simulated…
Genuine signal obtained
Out-of-control-process
Estimate the process change point using the proposed and alternative methods
Notes: Once the in-control parameters were estimated, monitoring began on the (M+1) st observation where a change in location (or scale) was simulated at 𝜏, so that observation 𝑀+𝜏+1 was the first observation sampled from the out-of-control process. Monitoring continued until a genuine signal was obtained at time M+T (T>=𝜏 +1)

## Slide 7
Empirical CDFs (ECDFs) of the CUSUM, proposed, and Perry and Pignatiello change point estimators following a genuine signal from the median-clipped CUSUM control chart of Perry and Wang. The CUSUM and proposed estimators were applied to the median-clipped sequence, while the Perry and Pignatiello estimator was applied to the continuous sequence, i.e., AR(1) with . ECDFs based on 10,000 independent simulation runs. is the magnitude of location shift in standard deviation units. .
Defense and Aerospace Test and Analysis Workshop
Zhi Wang
April 27, 2022
7/10
Performance and Recommendation
Notes: In summary, the proposed and CUSUM change point estimators are more robust to the skewness of the error distribution and changes in the magnitude of 𝛽. Additionally, since the true magnitude of change b is rarely known, having a change point estimator that yields robust performance across various levels of b would be beneficial in practice. Consequently, because the proposed estimator generally outperforms the CUSUM estimator, we recommend using the proposed estimator in practice, unless 𝛽 is assumed to be moderate-to-large(say, 𝛽 > 1:5). For larger 𝛽, the Perry and Pignatiello [8] estimator generally performs best.

## Slide 8
Defense and Aerospace Test and Analysis Workshop
Zhi Wang
April 27, 2022
8/10
Illustrative Example
Illustrative Example
Demonstrate our new change point estimator on the selective laser melting (SLM) process discussed in Colosimo
and Grasso.
  Problem: hotspot occurrences in a laser powder bed fusion (LPBF) process
  Data: Monitoring data are collected by video capture of the process, where any given video can be broken down into a time series of frames.
    Rate of capture: 32 frames per second
    Each frame consists of a 71121 matrix of
Figure shows the triangle shape being manufactured for this example, with the three corners identified by X, Y, and Z. Note that Figure 7a reports the pixels considered within each frame (or matrix), while Figure 7b identifies the laser melting tool along with the hotspot that occurred at pixel Z.
Figure plots the time series extracted from each of the three pixels

## Slide 9
Defense and Aerospace Test and Analysis Workshop
Zhi Wang
April 27, 2022
9/10
Illustrative Example
Figure shows the median- and IQR-clipped CUSUM charts applied to pixel Z, for both the increasing and decreasing cases.
The CUSUMs were designed for a 50% increase/decrease in the mean of the clipped process
The alarm threshold for each chart was set so that the joint monitoring scheme yielded an in-control ARL of approximately 1000
Both CUSUM charts were designed under a first-order Bahadur approximation to the clipped sequences
Notice that the median-clipped CUSUM for increases produced a signal at frame 114, while the IQR-clipped CUSUM produced a signal at frame 133

## Slide 10
Defense and Aerospace Test and Analysis Workshop
Zhi Wang
April 27, 2022
10/10
Illustrative Example
Figure shows Change point estimates using (a) CUSUM estimator and (b) proposed estimator. Horizontal lines in log-likelihood vs potential change point plots in (b) represent the 95% critical value for the confidence set, i.e., all t that yield log-likelihood values above the horizontal line are included in the 95% confidence set.
Given that the true process change occurred around frame 100:
The CUSUM approach estimated an increase in process location following frame 84 and a decrease in process scale following frame 99
The proposed approach estimated a location increase following frame 94, and a scale decrease following frame 99
Box and Cox [3] suggested constructing confidence sets on parameter estimates using the likelihood function. Applying such a method yields an approximate confidence set of the form
The cardinality of the confidence set for a location shift is 14, while set cardinality for a scale shift is 6, suggesting greater variability in the estimate for the time of location shift.
Notes: As mentioned earlier, one additional advantage to using the proposed change point estimator as an alternative to the CUSUM estimator is that an approximate confidence set can be constructed on the true change point
where 𝜒_(1,𝛼)^2is the upper a quantile of the chi-square distribution with one degree of freedom.
If the value of the log likelihood function at 𝑡, 𝑙_1 (𝑡), exceed the maximum of the log-likelihood function – the reference value, then t is included in the confidence
set. Note that the reference value suggested here is based upon the asymptotic distribution of the likelihood ratio statistic, e.g., see Wilks [13]. Figure (b) shows horizontal line for this value for both the location and scale cases.

## Slide 11: Thank You !