## Slide 1
A Reliability Assurance Test Planning and Analysis Tool
Presenter: Emma Mitchell
Co-Authors: John Haman, Rebecca Medlin, Curtis Miller, Dhruv Patel, and Keyla Pagán-Rivera
DATAWorks 2025

## Slide 2: Bottom Line Up Front
?
Motivation
Problem
Project Goal
We would like to size a test for evaluating system reliability.
We would like to incorporate prior knowledge of the system.
It is often difficult to scope a test that is long enough to ensure adequate assessment of system reliability.
No user-friendly software to implement prior data into reliability assurance test.
Develop an R Shiny app for the Test Science website
Planning: Use Bayesian methods to leverage supplementary data when determining appropriate test length, which may reduce testing.
Analysis: Use Bayesian methods to combine information and better quantify uncertainty through credible intervals.
Outcome
A Bayesian reliability tool for T&E community to use in reliability planning and analysis.

## Slide 3
Big Picture – What is Reliability and Why is it Important to T&E?
MTBF – Mean Time Between Failures
Importance
Definition
Reliability
Probability that a system performs its intended function under operating conditions for a specified period of time.
The reliability quantity of interest is typically the MTBF.
Example: We want an elevator to be reliable, meaning it should consistently operate without getting stuck during normal usage over time.

## Slide 4
Definition
Reliability
An unreliable system may impact the mission, resulting in errors, delays, or even accidents.
Unreliable systems also increase system costs over time.
Planning a test with reliability in mind will inform us which systems are robust, cost-effective, and capable of meeting operational demands.
Big Picture – What is Reliability and Why is it Important to T&E?
MTBF – Mean Time Between Failures
Importance
Notes: If we plan a test with reliability in mind we can hopefully prevent against having an unreliable system as out end product

## Slide 5: Case Study: Testing a New Variant of a Cargo Helicopter
Supports a variety of operations, such as:
Air movement (e.g., carry cargo, personnel)
Casualty evacuation
Aerial recovery
Area resupply

## Slide 6: Case Study: Testing a New Variant of a Cargo Helicopter
MTBF – Mean Time Between Failures
Reliability requirement of 35 flight hours MTBF.
Reliability objective of 70 flight hours MTBF.
Prior developmental testing included 329 flight hours and 7 mission failures.
Some system changes might imply an estimated 10 to 30 percent decrease in reliability from DT to OT.
How long should we test the helicopter, and what should be the maximum number of failures allowed when demonstrating the requirement with confidence?

## Slide 7: Reliability Demonstration Test – The Traditional Approach to Test Planning
A reliability demonstration test assumes we will use only the data from the current test to assess whether the reliability quantity of interest (e.g., MTBF) meets or exceeds the requirement.
An Operating Characteristics Curve is a useful tool for determining and comparing reliability plans.
  The test length is informed by:
    The reliability requirement
    The system’s true reliability
    The risk we are willing to accept in making an incorrect statement about the system’s reliability
MTBF – Mean Time Between Failures
A Reliability Demonstration Test often requires lengthy testing periods or a very high true MTBF. (Unlikely!)
Chart: True MTBF (Flight Hours)
Test Length 1 MTBF goal
Probability of Acceptance Level | 0.7 | 0.7
95-hour MTBOMF Goal | 0 | 1.1
69-hour MTBOMF Requirement | 0 | 1.1
Notes: If we choose the shortest test plan which requires 105 hours of testing, we can see we would need a true MTBF of around 95 flight hours to have a high probability of demonstrating reliability. However a true MTBF of 95 flight hours is unlikely since it is larger than even our objective (70). In order to avoid making an unlikely assumption about the true reliability we would require a much longer testing period.

## Slide 8: Reliability Assurance Test – A Bayesian Approach to Test Planning
A Bayesian reliability assurance test uses all contextual information with the goal of reducing the required amount of testing.
Contextual information includes:
- Earlier test results on the same or similar systems
- Expert judgment regarding performance
- Knowledge of the environmental conditions under which the systems are used
- Prior knowledge of possible failures
A Bayesian reliability assurance test often works best when…
- Minimal system changes expected between testing
- Longer previous testing periods
- Proposed test length from a reliability demonstration test is not feasible

## Slide 9: Bayesian Reliability Assurance test plans are more efficient than traditional Reliability Demonstration Plans in this case study.
Chart: Number of allowed mission failures (c)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
RDT | 56 | 105 | 150 | 193 | 235 | 277 | 318 | 358 | 398 | 438 | 478 | 517
BAT | 43 | 67 | 93 | 119 | 145 | 171 | 199 | 225 | 253 | 279 | 307 | 335
Comparing Traditional and Bayesian Test Plans: Prescribed Flight Hours by Number of Allowed Failures
Bayesian Test Length
Traditional Test Length
Test Plan Prescribed Flight Hours
Notes: Now that we have talked about both the RDT and BAT, we can compare the approaches using our helicopter case study

## Slide 10
    Comparing the Expected Bayesian and Traditional Reliability Estimates with 80% Intervals for each Specified Test Plan
Bayesian Reliability Test Plans (flight hours (fh), failures)
(199 fh, 6)
(171 fh, 5)
(145 fh, 4)
(119 fh, 3)
(93 fh, 2)
(67 fh, 1)
0 100 200 300 400 500 600
MTBF
Bayesian Interval
Traditional Interval
MTBF: Mean Time Between Failure
Incorporating previous test data reduces uncertainty around the MTBF estimates.
Notes: If we observe a test exactly like what we planned for, the interval produced by incorporating previous test data shown in blue is always contained within the interval constructed using traditional methods. This means incorporating previous testing data reduced uncertainty around the MTBF estimates and gives a better understanding of the helicopter's reliability.

## Slide 11: Bayesian Reliability Assurance Test – What are the steps?
Step 3: Solve for test plans.
Step 1: Define the prior, likelihood, posterior, threshold , and objective . Determine whether a change (degradation or improvement) from one testing phase to another is likely.
Step 2: Determine the maximum amount of producer and consumer risk you are willing to take.
Step 4: Compute the unconditional probability of passing for each test plan.
Reliability Assurance Test

## Slide 12: Bayesian Reliability Assurance Test – What are the steps?
Step 3: Solve for test plans.
Step 1: Define the prior, likelihood, posterior, threshold , and objective . Determine whether a change (degradation or improvement) from one testing phase to another is likely.
Step 2: Determine the maximum amount of producer and consumer risk you are willing to take.
Step 4: Compute the unconditional probability of passing for each test plan.
Reliability Assurance Test

## Slide 13
failures from DT
mission failure
(Prior)
(Likelihood)
(Posterior)
DT – Developmental Testing; MTBF – Mean Time Between Failures
First, define the Prior, Likelihood, and Posterior…
The posterior is the updated distribution of MTBF given our supplemental data and will serve as our prior belief about MTBF when we solve for a test plan.
i.i.d.

## Slide 14: Bayesian Reliability Assurance Test – What are the steps?
Step 3: Solve for test plans.
Step 1: Define the prior, likelihood, posterior, threshold , and objective . Determine whether a change (degradation or improvement) from one testing phase to another is likely.
Step 2: Determine the maximum amount of producer and consumer risk you are willing to take.
Step 4: Compute the unconditional probability of passing for each test plan.
Reliability Assurance Test

## Slide 15: … And determine whether a change (i.e., a degradation or improvement) from one test phase to another is likely.
Failing to incorporate a degradation factor could lead to inadequate test plans.
Source: Gilman, J. F., Fronczyk, K. M., & Wilson, A. G. (2018). Bayesian modeling and test planning for multiphase reliability assessment. Quality and Reliability Engineering International, 35(3), 750-760. https://doi.org/10.1002/qre.2406
Operational Testing (OT):
Production-representative systems.
Conducted in operationally realistic environment.
Tested by real users.
Duration of testing is often limited.
Example Phases: DT to OT
Developmental Testing (DT):
Usually conducted in a more controlled environment.
Tested by non-operationally representative users.
Testing is often longer, with a focus on verifying system requirements.
Deg./Imp. Factor
Original MTBF Posterior
Adjusted MTBF
MTBF
Density
Adjusted Posterior
Original Posterior
Threshold Requirement
Objective Requirement
Legend
Original MTBF Prior
Original Likelihood
i.i.d.

## Slide 16: Bayesian Reliability Assurance Test – What are the steps?
Step 3: Solve for test plans.
Step 1: Define the prior, likelihood, posterior, threshold , and objective . Determine whether a change (degradation or improvement) from one testing phase to another is likely.
Step 2: Determine the maximum amount of producer and consumer risk you are willing to take.
Step 4: Compute the unconditional probability of passing for each test plan.
Reliability Assurance Test

## Slide 17: Second, choose the maximum amount of risk you are willing to take.
MTBF – Mean Time Between Failures
Posterior Producer’s Risk: The risk of having an MTBF above the objective , given the test was failed.
Context: If the test is failed, the producer requires there to be no more than an percent chance that the true MTBF of the helicopter is greater than flight hours.
Posterior Consumer’s Risk: The risk of having an MTBF below the threshold requirement , given the test was passed.
Context: If the test is passed, the consumer requires that there be no more than a percent chance that the true MTBF of the helicopter is less than flight hours.
The system passes the test if we observe c or fewer failures in total operating time T.

## Slide 18: Bayesian Reliability Assurance Test – What are the steps?
Step 3: Solve for test plans.
Step 1: Define the prior, likelihood, posterior, threshold , and objective . Determine whether a change (degradation or improvement) from one testing phase to another is likely.
Step 2: Determine the maximum amount of producer and consumer risk you are willing to take.
Step 4: Compute the unconditional probability of passing for each test plan.
Reliability Assurance Test

## Slide 19: Solve for a Test Plan
C – Maximum allowed number of failures; PCR – Posterior Consumer’s Risk; PPR – Posterior Producer’s Risk
Operating Time (T)
Chosen T for a c = 2 failure test
Probability
PPR and PCR Plot for a 2 Failure Test
For each c, the chosen test is the shortest test that satisfies both PPR and PCR requirements:

## Slide 20: Bayesian Reliability Assurance Test – What are the steps?
Step 3: Solve for test plans.
Step 1: Define the prior, likelihood, posterior, threshold , and objective . Determine whether a change (degradation or improvement) from one testing phase to another is likely.
Step 2: Determine the maximum amount of producer and consumer risk you are willing to take.
Step 4: Compute the unconditional probability of passing for each test plan.
Reliability Assurance Test

## Slide 21: UPPT determines how likely your system is to pass
OT – Operational Testing; DT – Developmental Testing; UPPT – Unconditional Probability of Passing Test
Low UPPT (<.5)
Good UPPT (between .5 and .9)
High UPPT (>.9)
UPPT can be used to help the evaluator choose a test plan in a situation where multiple test plans meet both PPR and PCR thresholds.
Low UPPT is bad: The system will likely fail future tests.
Historical data indicate low reliability.
Test plan is inadequate.
Requirements are stringent.
High UPPT is suspicious: The system will likely pass future tests.
Historical data indicate high reliability.
Test plan requires lots of testing.
Requirements are lenient.

## Slide 22: Low UPPT Example
If …
Then regardless of …
= Small UPPT (<.5)
0 allowed MF
43 hours
DT Data
7 MF
329 hours
Test Plan
35 hours (MTBF)
Requirement
1 MF in 43 hours = 43 hours (MTBF)
OT Data
Decision
DT – Developmental Testing; MF – Mission Failures; MTBF – Mean Time Between Failures; OT – Operational Testing; UPPT – Unconditional Probability of Passing Test
FAIL
Notes: P(I observe ≤0 fails in 33 hrs of OT testing given I observed 6 mission aborts and 245 hrs of testing)
Dt data is how well you think your child is intellectually
Requirement is they have a B average
If you send them to a school where they wont be challenged they may be val..

## Slide 23
Once the prior is defined, my app provides evaluators with:
Credible intervals that define the range within which the true MTBF is likely to lie
A probabilistic assessment of whether the system meets the established requirements
MTBF – Mean Time Between Failure
What does analyzing data from a Bayesian Assurance Test Provide Evaluators?
Credible Interval
Probability Greater than Requirement

## Slide 24: Plan with Ease

## Slide 25
Plan with Ease – Perform a Bayesian Assurance Test using my app
DT – Developmental Testing ; MTBF – Mean Time Between Failures
DT Data

## Slide 26
Plan with Ease – Perform a Bayesian Assurance Test using my app
DT – Developmental Testing ; MTBF – Mean Time Between Failures
Minimum acceptable reliability and desired reliability
DT Data

## Slide 27
Plan with Ease – Perform a Bayesian Assurance Test using my app
DT – Developmental Testing ; MTBF – Mean Time Between Failures
Minimum acceptable reliability and desired reliability
DT Data
Amount of risk we are willing to accept for making a wrong decision

## Slide 28
Plan with Ease – Perform a Bayesian Assurance Test using my app
DT – Developmental Testing ; MTBF – Mean Time Between Failures
Minimum acceptable reliability and desired reliability
DT Data
Amount of risk we are willing to accept for making a wrong decision
What is the longest test time and largest number of failures you are willing to consider in the test plan?

## Slide 29
Plan with Ease – Perform a Bayesian Assurance Test using my app
DT – Developmental Testing ; MTBF – Mean Time Between Failures
What is the longest test time and largest number of failures you are willing to consider in the test plan?
Minimum acceptable reliability and desired reliability
DT Data
We know there are some system changes from DT to OT
Amount of risk we are willing to accept for making a wrong decision

## Slide 30
PPR – Posterior Producer’s Risk ; PCR – Posterior Consumer’s Risk; UPPT – Unconditional Probability of Passing Test
Plan with Ease – Perform a Bayesian Assurance Test using my app
All test plans have PPR less than .3

## Slide 31
PPR – Posterior Producer’s Risk ; PCR – Posterior Consumer’s Risk; UPPT – Unconditional Probability of Passing Test
Plan with Ease – Perform a Bayesian Assurance Test using my app
All test plans have PPR less than .3
…and PCR less than .2

## Slide 32
PPR – Posterior Producer’s Risk ; PCR – Posterior Consumer’s Risk; UPPT – Unconditional Probability of Passing Test
Plan with Ease – Perform a Bayesian Assurance Test using my app.
All test plans have PPR less than .3
…and PCR less than .2
Tradeoff between long test plans with little risk and shorter test plans with higher risk

## Slide 33
PPR – Posterior Producer’s Risk ; PCR – Posterior Consumer’s Risk; UPPT – Unconditional Probability of Passing Test
Plan with Ease – Perform a Bayesian Assurance Test using my app.
All test plans have PPR less than .3
…and PCR less than .2
Tradeoff between long test plans with little risk and shorter test plans with higher risk
Not all test plans have a good UPPT

## Slide 34: Analyze with Ease

## Slide 35
PPR – Posterior Producer’s Risk ; PCR – Posterior Consumer’s Risk; UPPT – Unconditional Probability of Passing Test
Analyze with Ease – Analyze Data from a Bayesian Assurance Test using my app

## Slide 36
MTBF – Mean Time Between Failures
Analyze with Ease – Analyze data from a Bayesian Assurance Test using my app
Statistical Interpretation:
There is an 80 percent probability the true MTBF falls within 29.77 and 57.55.
There is a 73 percent chance the true MTBF is greater than the threshold requirement.,
The estimated MTBF (mean of posterior) is 43.26.

## Slide 37: Closing Remarks
RDT – Reliability Demonstration Test; BAT – Bayesian Assurance Test; MTBF – Mean Time Between Failures
Bayesian assurance test plans can be more efficient than traditional reliability demonstration test plans.
Incorporating previous testing data can reduce uncertainty for the MTBF estimate.
The app I developed provides OED researchers a simple and convenient way to implement Bayesian assurance testing.
    Comparing the Expected Bayesian and Traditional Reliability Estimates with 80% Intervals for each Specified Test Plan
Bayesian Reliability Test Plans (flight hours (fh), failures)
(199 fh, 6)
(171 fh, 5)
(145 fh, 4)
(119 fh, 3)
(93 fh, 2)
(67 fh, 1)
0 100 200 300 400 500 600
MTBF
Bayesian Interval
Traditional Interval
Chart: Number of allowed mission failures (c)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
RDT | 56 | 105 | 150 | 193 | 235 | 277 | 318 | 358 | 398 | 438 | 478 | 517
BAT | 43 | 67 | 93 | 119 | 145 | 171 | 199 | 225 | 253 | 279 | 307 | 335
Comparing Traditional and Bayesian Test Plan Prescribed Flight Hours by Number of Allowed Failures
Bayesian Test Length
Traditional Test Length

## Slide 38
Future Work
Publish R Shiny Application on Test Science Website.
Author a paper for The ITEA Journal of Test and Evaluation to increase awareness of method/application.
Extend to additional failure time distributions (e.g., Weibull).

## Slide 39: References
Gilman, J. F., Fronczyk, K. M., & Wilson, A. G. (2018). Bayesian modeling and test planning for multiphase reliability assessment. Quality and Reliability Engineering International, 35(3), 750-760. https://doi.org/10.1002/qre.2406
Hamada, M. S., Wilson, A. G., Reese, C. S., & Martz, H. F. (2008). Bayesian reliability. Springer. https://doi.org/10.1007/978-0-387-77950-8

## Slide 40: Backup

## Slide 41: So the second step is to decide on the maximum allowable producer and consumer risk you would like to take
Posterior Consumer’s Risk: The probability the system’s reliability is worse than the MTBF requirement, given the test is passed and historical data on the system’s reliability.
Where is available historical data and is the number of draws from the posterior given our historical data
Note: The expression Test is Failed means that the number of observed failures is larger than the maximum number of allowed failures. That is, . Similarly, Test is Passed means that .
PPR
PCR
Source: Michael S. Hamada et al., Bayesian Reliability, 2008, Chapter 10.

## Slide 42: So the second step is to decide on the maximum allowable producer and consumer risk you would like to take
Note: The expression Test is Failed means that the number of observed failures is larger than the maximum number of allowed failures. That is, . Similarly, Test is Passed means that .
PPR
PCR
Source: Michael S. Hamada et al., Bayesian Reliability, 2008, Chapter 10.
Posterior Producer’s Risk: The probability the system’s reliability is better than the MTBF objective, given the test is failed and historical data on the system’s reliability.
Where is available historical data and is the number of draws from the posterior, given the historical data.

## Slide 43: What does the Reliability Belief Distribution indicate?
Previous testing suggests reasonable reliability after degradation. A reliability assurance test may be useful.
Updated distribution of mean time between failure, given DT data
Transformed = 10-30% degradation

## Slide 44: What can we say about the true MTBF if we implement one of these test plans?
MTBF – Mean Time Between Failures
The analysis tab of the app allows the user to...
Quantify uncertainty around the true MTBF with credible intervals
Determine the probability of meeting the minimal acceptable reliability and desired reliability
Characterize the distribution of the MTBF given our prior beliefs/data
Compare the uncertainty around the estimated MTBF across multiple test plans and/or prior beliefs

## Slide 45
The app allows evaluators to select one of three different priors for the MTBF All models assume i.i.d. exponential between failure times.
Pull prior from planning tab:
(prior)
(posterior)
Enter prior based on historical data:
(prior)
(posterior)
where
Uninformative prior:
(prior)
(posterior)
How to analyze data from a Bayesian Assurance Test
Posterior
Prior
+ Observe test data
+ Update for next test phase