## Slide 1: Cost Considerations for Estimating SmallSat I&T
2024 DATAWorks: Defense and Aerospace Test and Analysis Workshop
Dr. Kathy Kha & Rachel Sholder
The Johns Hopkins Applied Physics Lab (JHU/APL)
Parametric Cost Analysts

## Slide 2: Background
In the early phases of project formulation, mission integration and test (I&T) costs are typically estimated via:
  A wrap factor approach
  Analogies to similar missions adjusted for mission specifics
  Bottom Up Estimate (BUE)
This wrap factor approach involves estimating mission I&T costs as a percentage of payload and spacecraft hardware costs
  This percentage is based on data from historical missions, with the assumption that the project being estimated shares similar characteristics with the underlying data set used to develop the wrap factor
This technique has worked well for traditional spacecraft builds, but with the emergence of CubeSats and nanosatellites, the cost basis of hardware is just not large enough to use the same approach
This suggests that there is a cost “floor” that covers basic I&T tasks such as a baseline of labor and testing

## Slide 3: Hypothesis
When we look at constellations of SmallSats, we begin to see cost sharing between SmallSats in the same constellation
With the evolution of new technologies, the way we estimate costs needs to evolve as well
Our research will examine approaches to estimating I&T costs when the base hardware cost is much lower than a traditional space science mission, making historical wrap factors inapplicable
Since SmallSats are generally simpler, less complex, and cheaper hardware, the cost of integrating multiple identical hardware elements isn’t accurately reflected
The objective is to use these results to develop a Cost Estimating Relationship (CER) that can better predict SmallSat I&T costs

## Slide 4: Methodology: Data Collection & Normalization
Cost and mass data was collected via CADRe
  Looked at missions with total hardware mass (payload + SC) of <180** kg (per small satellite)
All costs inflated to FY$24 using NASA New Start Inflation Index
Costs for I&T include integration of the spacecraft subsystems and instruments
**Mabrouk, Elizabeth. What Are SmallSats AND CUBESATS? www.nasa.gov/content/what-are-smallsats-and-cubesats.

## Slide 5: Methodology: Parameters
With the objective being to develop a parametric CER that calculates I&T costs for small satellites, the following variables were considered
Due to a limited dataset and previous success, we focused on one parameter that incorporates many of the other ones

## Slide 6: Previous Points of Integration Work
Drew motivation from and leveraged previous work looking at I&T costs for historical APL missions**
**Powers, N. "Analysis of Integration and Test (I&T) Costs for Recent NASA Missions." AIAA/San Diego Aerospace Conference, 2014.
Notes: Lognormal curve is chosen due to expected savings with more integrated points

## Slide 7: Justification for a SmallSat Specific CER
Ran the 5 missions in this analysis through the existing I&T CER
We see negative costs for single unit missions with low points of integration and extreme overestimates for multiple unit missions with many points of integration
Thus, there could be a specific SmallSat CER due to I&T savings

## Slide 8: SmallSat Savings
We also know there are I&T savings based on industry data
  Average of 23% savings per additional unit (I&T costs)
Created a logarithmic model using total points of integration
  Savings accounted for in the model selection
Created a linear model using weighted points of integration
  Savings accounted for in the input data
Notes: Logarithmic model assumes a learning curve

## Slide 9: Points of Integration Calculation
Total Points of Integration Calculation:
  Count up the number of spacecraft subsystems across all spacecraft
  Count up the number of instruments across all spacecraft
  Example:
    6 Subsystems + 2 instruments = 8 points of integration
    8 points of integration * 4 copies = 32 total points of integration
Weighted Points of Integration Calculation:
  Count up the number of spacecraft subsystems across all spacecraft
  Count up the number of instruments across all spacecraft
  Apply 77% (industry average) copy factor to any additional copies
  Example:
    6 Subsystems + 2 instruments = 8 points of integration
    8 points of integration * 4 copies * 77% = 26 weighted points of integration

## Slide 10: Total Points Model
The above chart shows the results of the regression analysis of the total points of integration vs. costs
Chart: SmallSat I&T Points of Integration CER
| 8 | 90 | 8 | 64 | 48
I&T Costs (FY$24K) | 1751 | 7696.554 | 1761.7507 | 10032.071 | 3691.548
Notes: - Logarithmic model assumes a learning curve
- Mission 4 and 5 not captured as well
- Nicole’s work was based on APL internal data where we had a clear view of the data points and could gather more information. We don’t have the same clarity into CADRe data. SmallSats capture a wider range of mission types (i.e. CubeSat constellations via COTS busses through custom builds like Swales for THEMIS, etc. so there’s more inherent variability in that too)

## Slide 11: Weighted Points Model
The above chart shows the results of the regression analysis of the weighted points of integration vs. I&T costs
Chart: SmallSat I&T Points of Integration CER
| 8 | 73.44 | 8 | 51.120000000000005 | 38.799999999999997
 | 1751 | 7696.554 | 1761.7507 | 10032.071 | 3691.548

## Slide 12: Test for Heteroscedasticity
No quantitative pattern to residuals (trendline on the x-axis)
Errors are uncorrelated and distributed normally (constant variance)
 Thus, the model is homoscedastic
Chart: Residuals as a Function of I&T Costs (Weighted)
| 1900.3157112257479 | 9146.4927029058217 | 1900.3157112257479 | 6674.9971275039388 | 5310.8024371387401
Residuals | -149.3157 | -1449.9387 | -138.565 | 3357.0739 | -1619.2544
Notes: - explain that it’s a good predictor for this data set but probably is limited to things in this range since we have such a small data set, etc etc it should definitely not be used for some huge constellation of like 12 cubesats or something

## Slide 13: Predictability
Both CERs have low prediction errors
 They are both accurately accounting for I&T savings

## Slide 14: Conclusions
We have reason to estimate I&T costs for small satellites differently than typical missions with larger hardware bases
However, the models that we currently have could be improved
The limited dataset prevents us from finding stronger statistical relationships and identifying statistically significant variables
  Need more data

## Slide 15: Suggestions for Future Research
Some diagnostic tests revealed a distinction between who performed I&T (university, NASA, contract) but there was no statistically significant relationship
  Need more data in order to articulate a statistically significant difference
With the rise of New Space organizations (i.e. Blue Canyon Technologies, Astranis) getting involved in the development of SmallSats, there may be an efficiency inherent in their processes that aren’t experienced by more traditional space organizations. This would be reflected in their I&T costs as well.
Notes: Theories include: graduate students being cheaper than FT engineers compared to contracting fees for outsourcing

## Slide 16: Suggestions for Future Research
Created a wrap factor CER looking at I&T as a percentage of hardware compared to the total points of integration for constellations of SmallSats
This showed a strong relationship
  Need more data to see if this relationship holds
Chart: I&T % vs Total Points of Integration
| 90 | 64 | 48
I&T % | 0.070475 | 0.15628 | 0.17394

## Slide 17: Suggestions for Future Research
Mass appears to be a good predictor of total points of integration and I&T costs
  Need more data
Combining the two, mass can be used to predict total points of integration which then predicts I&T costs
Chart: Total Points of Integration CER
| 60.4 | 379.7 | 10.4 | 304.89999999999998 | 32.04
Total Points of Integration | 8 | 90 | 8 | 64 | 48
Chart: I&T Costs CER
| 60.4 | 379.7 | 10.4 | 304.89999999999998 | 32.04
I&T Costs (FY$21K) | 1751 | 7696.554 | 1761.7507 | 10032.071 | 3691.548
Chart: I&T Costs (FY$24K)
| 25.930799999999998 | 84.043400000000005 | 16.8308 | 70.4298 | 20.769280000000002
I&T Costs (FY$21K) | 1751 | 7696.554 | 1761.7507 | 10032.071 | 3691.548