## Slide 1: Combinatorial and Adaptive Stress Testing for Spacecraft Runtime Assured Neural Network Control Systems
Gabriel Behrendt Alexandra Mangel
Kerianne Hobbs
Todd Moeller
DATAWorks April 21-23, 2026
Approved for public release. OTR 2026-00517.

## Slide 2: Trustworthy Autonomous Systems Require Rigorous Testing
Neural Network Control Systems (NNCS)
Powerful approach for complex autonomous systems
Learn optimal policies from data and handle high dimensional state spaces
Challenge: Learned complexity creates unpredictability where small variations cause dramatically different behavior
Safety Approaches & Limitations
Theoretical guarantees (reachability analysis, differential dynamic logic, certificate functions)
  Limited to small state spaces and short time horizons
Runtime Assurance (RTA): Monitors system state and controller output, intervenes when necessary
Challenge: Real-world implementations face discretization effects and numerical precision limitations
The Testing Challenge
Establishing trustworthiness requires knowledge of operational boundaries, edge cases, and failure modes
Existing approaches may be inadequate for complex systems
Our Goal: A Rigorous Testing Framework
Thorough initial state space coverage
Targeted exploration of operational boundaries and edge cases

## Slide 3: Our Proposed Testing Approach for Complex Systems
Our Proposed Approach
Combinatorics generated t-way initial conditions reduces dimensionality of sampling
Adaptive stress testing (AST) will target critical regions by intelligently selecting disturbances
Comprehensive testing of complex systems presents two distinct challenges to uncover failure modes:
Thorough coverage of the initial state space
Systematic exploration of system behavior under stressing conditions
Problems with Current Approaches
Traditional Monte Carlo testing approaches rely on random sampling to address the challenges above, but:
High-dimensional state spaces challenge random sampling approaches because volume grows exponentially with dimension
The systematic targeting of critical regions near safety boundaries where failures are likely to occur does not occur with random sampling
System under test - satellite attitude control system

## Slide 4: System Under Test - Autonomous Satellite Attitude Control System
Two reference frames
  Body frame
  Hill frame
Relevant vectors
  Sensor pointing vector
  Mission vector
  Sun vector
  Command vector (generated by neural network)
Successful mission execution
Safety functions (enforced by runtime assurance filter)
Inclusion Zone
Exclusion Zone
Mission: align the sensor pointing with the mission vector while avoiding the sun vector to avoid mission critical sensor damage

## Slide 5: Runtime Assured Neural Network Control System Architecture
The RL agent generates pointing commands based on the spacecraft state
The commands are translated to nominal torque inputs by a Proportional-Derivative Controller
To monitor safety, a Control Barrier Function (CBF) based RTA filter monitors and modifies the nominal torques when necessary to fulfill safety constraints
Neural Network*
PD Controller
RTA
Observer
Spacecraft Dynamics
RL Agent (0.05 Hz)
Feedback Control Loop (1 Hz)
nom
RTA
To increase the trustworthiness of this runtime assured NNCS we must propose a testing framework which tests its operational boundaries and finds edge cases through (1) initial state space coverage and (2) targeted disturbances
* Santos, Raul, et al. "Deep Reinforcement Learning Waypoint Generation for Attitude Station-Keeping With Sun Avoidance." AIAA SCITECH 2026 Forum. 2026.

## Slide 6: Initial Condition Generation with -way Testing
Core Concept: Tests all possible combinations of any parameters (instead of all parameters)
Key Benefit: Drastically reduces test cases while maintaining coverage
  Example: testing covers all 3-way interactions in 4D quaternion space
  Achieves ~10x reduction vs. exhaustive testing
Why It Works: Most failures triggered by interactions of few parameters (2-6), not all simultaneously
Application: Generate initial spacecraft attitudes with efficient coverage
Coverage Metrics
Quaternion Representation: Rotations mapped as points on unit sphere,
Voronoi Binning: Quantifies geometric coverage uniformly
Key Metrics: % occupied bins, mean occupancy, occupancy variance
What is -way Testing?*
*Kuhn, D. Richard, et al. "Combinatorial testing: Theory and practice." Advances in computers 99 (2015): 1-66

## Slide 7: Adaptive Stress Testing (AST)
Disturbance
AST Agent
Reward Function
Simulator
Next State
Reinforcement Learner
System Under Test
Environment
AST Framework: Casts failure search as Markov decision process using reinforcement learning*
Objective: Find most likely failure path by solving
RL Algorithms: MCTS, Q-Learning, deep RL to optimize disturbance sequences
Our Implementation: Monte Carlo Tree Search with Progressive Widening (MCTS-PW)
  Handles continuous action spaces
  Balances exploration of new disturbances with exploitation of promising failures
Two Test Configurations:
  Runtime Assurance Filter Testing
  Runtime Assured NNCS Testing
Monte Carlo Tree Search
*Lee, Ritchie, et al. "Adaptive stress testing of airborne collision avoidance systems." 2015 IEEE/AIAA 34th Digital Avionics Systems Conference (DASC). IEEE, 2015.

## Slide 8: Summary of Tests
We conduct two test configurations to assess our proposed approach vs. Monte Carlo approach
Configuration 1: Runtime Assurance Filter
Configuration 2: Runtime Assured NNCS

## Slide 9: Runtime Assurance Filter Testing
Initial state space: Attitude quaternions
Online adversarial input: Nominal torque inputs
Primary objective: Verify safety filter
Failure definition: Safety Constraint violation
Monte Carlo Approach
  Initial conditions:
  Nominal torque inputs:
Our Approach
  Initial conditions: Use combinatorics to generate 3-way tests
  of the 4-element quaternion
  Nominal torque inputs: Monte Carlo tree search with progressive widening (MCTS-PW)
Incentivizes safety constraint violation
Generate quaternions that sufficiently cover the initial state space
Find nominal torque inputs that explore and stress the system’s inclusion and exclusion zone
Testing Goals

## Slide 10: Runtime Assurance Filter Testing - Test Case Generation Results
Metric | T-way | Monte Carlo
Occupancy [%] | 5.0 | 5.4
Mean | 0.2 | 0.2
Variance | 1.03 | 0.85
T-way
Monte Carlo
Generated 99 valid test cases using -way and Monte Carlo methods
-way guarantees all 3-way parameter combinations; Monte Carlo relies on random chance
Can AST find failures Monte Carlo misses?
~5% occupancy due to geometric constraint, not sampling limitation
Key finding: -way and Monte Carlo achieve equivalent coverage (5.0% vs 5.4%) with 99 test cases
Implication: Both methods provide adequate initial state coverage
Notes: We should tell the audience how to interpret these results and give reason for them.

## Slide 11: Runtime Assurance Filter Testing
AST-Driven vs. MC-Random Torque Inputs
Key Finding: Adaptive stress testing finds and explores the boundary, while Monte Carlo rarely finds the boundary
Adaptive Stress Testing
Monte Carlo

## Slide 12: Runtime Assurance Filter Testing
Adaptive Stress Testing Found Failures Better Than Monte Carlo
AST found 6 violations of the exclusion zone and 13 violations of the inclusion zone across 99 trials
  Maximum violation :
  Maximum violation :
Monte Carlo testing with the same number of trials found zero safety violations
Though these violations are small instantaneously, some persisted multiple timesteps accumulating violations
  Maximum cumulative violation :
  Maximum cumulative violation :
Key Finding: Even with mathematical guarantees runtime assurance filters can be violated under adversarial conditions generated by AST that are missed by random testing
Can AST stress the complete integrated system - the neural network, the RTA filter, and the spacecraft dynamics all working together at different rates?
6 Violations
13 Violations

## Slide 13: Runtime Assured NNCS Testing
Initial state space: Mission and Sun angles
Online adversarial input: Angular velocity disturbances
Primary objective: Assess integrated RTA+NN performance
Failure definition: Mission degradation, safety violation, control effort
Monte Carlo Approach
  Initial conditions:
  Angular velocity disturbances:
Our approach
  Initial conditions: Same initial conditions as Monte Carlo Approach because t-way testing is trivial for a two-dimensional state-space
  Angular velocity disturbances: AST using MCTS-PW
The log likelihood of the probability incentivizes the MCTS-PW to select likely disturbances
Testing Goal: Find angular velocity disturbances that (1) degrade mission, (2) decrease safety margin, and (3) increase control effort

## Slide 14: Runtime Assured NNCS Testing Results
We run 100 unique initial conditions of for s
All spacecraft are initialized such that and
Baseline (no disturbances) vs. MC (random) vs. AST (targeted)
Mission Degradation : AST increased average mission deviation by (9 minutes lost mission time)
Safety Margin Reduction : AST reduced exclusion angle by vs. for MC
Increased Control Effort : AST disturbances forced RTA to produce highest magnitude torques
Key Insight: AST successfully stresses the integrated runtime assured NNCS beyond random testing
Mission Performance
Safety Margin
Control Effort

## Slide 15: Thank you

## Slide 16: References
Kuhn, D. Richard, et al. "Combinatorial testing: Theory and practice." Advances in computers 99 (2015): 1-66
Lee, Ritchie, et al. "Adaptive stress testing of airborne collision avoidance systems." 2015 IEEE/AIAA 34th Digital Avionics Systems Conference (DASC). Ieee, 2015.
Santos, Raul, et al. "Deep Reinforcement Learning Waypoint Generation for Attitude Station-Keeping With Sun Avoidance." AIAA SCITECH 2026 Forum. 2026.

## Slide 18: Runtime Assurance Filter Testing - Test Case Generation Results
Metric | T-way | Monte Carlo
Occupancy [%] | 5.0 | 5.4
Mean | 0.2 | 0.2
Variance | 1.03 | 0.85
T-way
Monte Carlo
Generated 99 valid test cases using -way and Monte Carlo methods
-way guarantees all 3-way parameter combinations; Monte Carlo relies on random chance
~5% occupancy due to geometric constraint, not sampling limitation
Implication: Both methods provide adequate initial state coverage
Key finding: -way and Monte Carlo achieve equivalent coverage (5.0% vs 5.4%) with 99 test cases
Can AST find failures Monte Carlo misses?
Notes: We should tell the audience how to interpret these results and give reason for them.