## Slide 1: CIVA NDT Simulation: Improving Inspections Today for a Better Tomorrow
Presented by Starr D’Auria
Extende Inc.

## Slide 2
1 : the act or process of simulating
2 : a sham object : counterfeit
3a : the imitative representation of the functioning of one system or process by means of the functioning of another.
Ex: a computer simulation of an industrial process
b : examination of a problem often not subject to direct experimentation by means of a simulating device
Examples of simulation in a Sentence
a computer simulation of spaceflight ; a simulation of the planet's surface
Definitions from
Merriam-Wester
Definition of Simulation
Notes: Ensure we have a common understanding on what simulation is

## Slide 3
Benefits of NDT Simulation
DESIGN, OPTIMIZE AND PREPARE INSPECTION:
  Evaluate a wide range of testing scenarios to converge on the optimal solution
  Master a technique with less iterations
  Test equipment effectiveness, including for options not yet purchased
  Less mock-ups, less trials : Save time and money
EXPERTISE:
  Reproduce field results to understand complex situations and confirm/disprove a diagnosis
QUALIFY:
  To support performance demonstrations with study of influential parameters by simulation (and reduce mock-up tests) 1) Predict the worst-case scenario 2) Compute POD curves: An element of technical justification in qualification stage
DISCUSS AND CONVINCE:
  To ease technical discussions between all “players” (inspector, manufacturer, engineer, material scientist, end user, etc.) and convince
TRAIN:
  Demonstrate the physics of NDT quickly and safely

## Slide 4
Ultrasonic Testing
    Beam Profile
    Inspection
Notes: Most have seen a UT simulation in the past, even if it is just ray trace
Not all of you aware of other simulation for other methods.
Providing overview of simulation of several different inspection methds

## Slide 5: Simulation of Component to be Inspected
Evaluate:
Shape of part
  Evaluate min/max conditions
Material
  Isotropic, anisotropic or composite
  Single or Multi-layer
  Grain structure
  Noise
  Attenuation
Notes: A variety of shapes that are either
In software menu and just dimensions need to be added
2D CAD extrusions
3D CAD imports
Shape
-min/ max allowed
-localized pitting or corrosion

## Slide 6: Flaw Geometry
Type of flaw geometries:
  Planar or crack-like flaws
  Inclusions
  Calibration reflectors
Evaluate:
Flaw shape
Flaw size
Flaw position
Flaw orientation
Determine ability of the proposed equipment to detect the flaw
Notes: The more accurately a flaw shape and orientation can be simulated, the closer the results are to experimental results

## Slide 7: UT Inspection Simulation - Scanning patterns
Evaluate
Start/Stop location of scan
Scanning direction
Data acquisition intervals
Step size between scan passes
Notes: Scan sim needed to accurately simulate experimental data
When planning robustness of inspection, use modeling to see if slight variations in starting postion and/or orientation have large effects on detection.
A very narrow beam may be great for sizing, but it easier to miss flaws if probe position and orientation is not dead on accurate

## Slide 8: UT Simulation - Transducers
Single Element, Dual Element and Phased-Array transducers types :
Immersion
Contact
Dual Element (TRL)
Flexible array probes
Notes: With ultrasound there are a large variety of probes that are used
Simulation needs to be able to cover the vast majority of probe types, shapes and sizes
Here you see simulated phased array transducers and corresponding real ones

## Slide 9
Coarse Grain Specimen
Isotropic Specimen
Evaluate:
Effects of grain structure on sound beam
Ability of sound to penetrate material
Changes in focusing
UT Beam Simulation – Coarse Grain
Notes: Grain structure has a large effect on how sound travels in a part. With simulation you can evaluation effects of different size grains
This slide illustrates the different between a part with small even sized grains and large ones that distort and scatter the sound
Simulation can also model the effects of elongated grains

## Slide 10: Stainless steel / Dissimilar weld material / Austenitic
UT Beam Simulation
Complex weld microstructure
Evaluate:
Ability of T45 wave to penetrate the weld
Ability of L45 wave to penetrate the weld
Conclusion:
  Longitudinal waves are
  significantly less affected
  than shear waves
Notes: With dissimilar metal welds it is always important to make sure you can get sound to penetrate the weld.
On right, traditonal T45. Sound largely stops at the metal/weld interface
On left, L45. Sound travels through the weld. With L45 there is also a shear component present.

## Slide 11: UT Inspection Simulation with Structural Noise
  Contact probe L45°
  Steel block of 20mm high
  Two flaws: 4 mm-high notch, 2-mm diameter SDH
  Planar Probe: SNR 10dB
  Cylindrical focusing: SNR 15dB
  Bifocal focusing: SNR 19dB
Evaluate:
Planar (Flat) Probe
Cylindrical focused Probe
Bifocal focused Probe
Conclusions:
The Bifocal probe had the best SNR at 19dB
With the flat probe it would be difficult to detect the notch above the noise level without risking a false positive
Notes: Use simulation to see which type of focusing has best SNR

## Slide 12
Radiography
Notes: Most have seen a UT simulation in the past, even if it is just ray trace
Not all of you aware of other simulation for other methods.
Providing overview of simulation of several different inspection methds

## Slide 13
RT Simulation
Evaluate
Radiation sources
Effects of scattered radiation
Filters
Relative positioning of source, component, flaws and detector
Image quality indicators
Teach
Effects of different material
Effects of exposure time
Relationship between flaw orientation and detection
Notes: Useful both for inspection planning and training,
For training, simulation provides a way to show effects of different equipment and setups without the hazards, constraints and regulations associated with real radiation
(either gamma or x-ray)

## Slide 14
RT Simulation
Images courtesy of Pessiki and Keller, Lehigh University
RT simulation of concrete block with embedded steel hardware
Effect of photon scattering and exposure time on image quality (200keV X-ray source)

## Slide 15
Partial implementation of the discrete aggregate
model in CIVA RT
Images courtesy of Pessiki and Keller, Lehigh University
Effect of the discrete aggregate model on
defect visualization
RT Simulation

## Slide 16
Evaluate
Sensor design:
  Geometry optimization
  addition of ferrite core
  shield ring
ET Probe Simulation
Notes: Like with UT, a large variety of probes can be simulated
-optimize sensor design
-determine if features such as ferrite cores of shielding rings improve results
Perform initial prototyping prior to physical probe prototyping

## Slide 17
Evaluate
Depth of Penetration
Field Size
Teach
Effects of material on depth of penetration
Effects of probe size on field
Effects of frequency on depth of penetration
ET Field Simulation
Notes: Easy to compare two probes

## Slide 18
Evaluate
Method design:
  Compare different sensors
  select the frequency
  define the acquisition channels (absolute, differential,…)
  set up calibration
  signal processing parameters (frequency mixing, etc.)
Determine Influential and/or disturbing parameters:
  Lift-off variation
  Sensor disorientation
  POD analysis, etc.
ET Inspection Simulation
Notes: Shows effectiveness or ineffectiveness of the chosen equipment and settings to detect flaws

## Slide 19
Evaluate
Modal displacements and constraints for each mode of each frequency within a given frequency range
Dispersion curve graphs, including for buried pipe
Affects of specific modes
GWT Modes Simulation
Dispersion curves…
  Wavenumber
  Wavelength
  Phase velocity
  Energy velocity
  Attenuation
…in order to get
  Modes available
  Mode selection
  Parameters of the probe
  Order of the echoes
  Time of flight
  Length under inspection

## Slide 20
Evaluate
Sound penetration in area of interest
Strength of field
GWT Field Simulation

## Slide 21
Evaluate
See how geometric discontinuities such as welds, grooves and diameter transitions effect flaw response
Predict flaw response for different size, shape, orientation and location of flaws
Evaluate the effectiveness of different transducers for specific configurations
GWT Inspection Simulation

## Slide 22
Parametric Studies
Evaluate
Variances in a parameter such as
  Flaw size, location and orientation
  Slight variations in equipment from nominal value
Relative influence of parameters (see next slide)

## Slide 23
Statistical distribution of input parameters
Graph of relative influence of the different parameters
Parametric Studies
Notes: Simulation assesses which variables have most significant impact on results
Which variables have little effect on results
-Focus on insuring key parameters are tightly controlled to maintain accuracy of results

## Slide 24
    Find most influential parameters:
  Run parametric variations to determine key parameters to focus on
    Optimize design of experiment:
  Fill in data gaps with simulated data
  Identify Key areas of uncertainty before making mock-up
    Examine uncertainties that can’t be determined experimentally
Model Assisted POD (MAPOD)
?
?
Missing values
Notes: Optimize: If measurements are not in the area of interest (defect size or range of variation of influential parameters not adapted), the result obtained with mock-ups are not reliable and cost increases!
Examine uncertainties: Parameters such as exact flaw location and orientation of embedded flaws are easy with a computer, but difficult if not impossible experimentally. There is always a tolerance on flaw position and orientation in mock-ups. When evaluating POD for small flaws, the variance may equal or exceed the size of the flaw to be evaluated
-slight variatiations in material properties such as velocity and density
-slight variations in equipment such as frequency of UT probe (2.05MHz instead of 2.00Mhz…)

## Slide 25
Use simulation to design for inspectability before designs are finalized
Simulate additional inspection methods, gaining the same benefits as simulation of existing methods
As computing power increases, it will become practical to run even complex models on laptops, supporting offline and remote modeling of inspections to assist field work
As connectivity increases, use of cloud computing and virtual computers will increase as a way to have the benefits of powerful computing without the need for a desktop computer
Future

## Slide 26
Starr D’Auria
Starr.dauria@extende.com
www.extende.com
https://www.youtube.com/user/extendechannel
Thanks for listening and learning!